## Slide 1: Monitoring and Management of Electrical Systems - an introduction (II) -
10.10.2014
02

## Slide 2
In the last decade of the 20th century, the electricity sector has undergone through major changes, because of the need of realigning it with the economical realities of the time.

## Slide 3: The Electricity Market
monopoly
free market

## Slide 4: The monopoly
production, transmission and distribution managed by and belonging to a single monopoly company
consumers charged by the monopoly company at regulated prices

## Slide 5: The free market
producers, transmission system operator, distribution operators, suppliers are independent, competing entities
pay scheme
    Producers to OTS
    Suppliers to producers, OTS and OD
    Consumers to suppliers
all consumers can choose their supplier and are charged at negotiated tariffs
the market is managed by an independent administrator, under the rules established by the regulatory authority

## Slide 6: In the mid 1990s…
the deregulated electricity market model was proposed, which promoted
    competition between producers
    competition between suppliers
    free (equality for all) trade of electricity
    lower prices
    possibility of choice for the consumers.

## Slide 7: …began the change
major changes in the way the electric power systems were operated
electricity was now sold and brought based on the basis of its price, rather than taking into account the optimal conditions which ensure the best security and efficiency in operation
less more

## Slide 8: New operation paradigm
power flows pattern changed, large quantities of power being directed from where the electricity was produced to where it was acquired, over very long distances, if required
systems previously not interconnected became part of a whole larger system – wide area power systems (WAPS)

## Slide 9: New challenges
renewable sources, encouraged by environmental concerns and promoted by market policies and financial subsidies.
    predictability: wind and solar radiation are unpredictable by nature
    size: range from very small (a few megawatts) to very large (thousands of megawatts)
    location: only in areas with maximum availability of wind and solar radiation,

## Slide 10: In EPS…
the term of control implies satisfying at all times certain technical requirements:
    the generated power must match the consumed power plus the power losses in the system
    the bus voltages must be as close as possible to the rated values of the bus voltages
    the generated active and reactive powers at generator buses must not exceed defined limits
    the line and transformer loads must not exceed the limit values over an extended period of time

## Slide 11: In EPS…
when an incident occurs in the system, its type, strength and location must be identified so that appropriate measures could be taken
when system parameters fall out of range, they must be corrected
These require monitoring

## Slide 12
the development of electricity markets and renewable resources changed the way systems are monitored and controlled
the differences can be studied by comparing some key aspects in the way systems were operated before and after the electricity market

## Slide 13: EPS operation, before
Economical aspects
  The economical aspects were managed at centralized level, by the vertically integrated national utility, which was, as a general rule, controlled by the state
  The principle was that all consumers must be supplied

## Slide 14: EPS operation, before
Technical aspects
    Systems were considered at local, regional, at most national level
    The system was managed in all its aspects (generation, transmission, distribution, consumption) by a single entity, which had a clear picture of everything that was going on in the system
    The operating conditions were more predictable and the required analysis tools were less complex
    The technical and security restrictions were the main concern in operation.

## Slide 15: EPS operation, after
Economical aspects
    The key principles in operating an energy market are profit and competition, which would ensure lower prices and liberty of choice for consumers.
    The production, transmission, distribution and supply utilities are unbundled activities carried out between players in direct competition on the market.
    The technical aspects of system operations are in direct conflict with the economical and environmental concerns, which are the core of the energy market.

## Slide 16: EPS operation, after
Technical aspects:
    Through interconnection, the systems became much larger and complex
    One of the essential conditions of the electricity market is the separation of production, transmission and distribution activities.
        Data availability at system level is often difficult or even impossible.
    Given the complexity of the system, the risk of failure and any other unpredictable events increases, and these could potentially affect a larger area, with heavier costs than before.
        means that more complex and fast analysis algorithms are required to assess the state of the system and take any necessary measures

## Slide 17: EPS operation, after
    Energy flows through the system change radically and can vary significantly from hour to hour, in parts of the system. Electricity is acquired based on the lower price principle and can travel a long way from where it’s produced to where it’s consumed.
        increased stress on the system.
    the distributed generation (small generation sources found on the consumer’s side), must be managed.
    renewable electricity sources such as wind and solar, are intermittent by their nature (sun doesn't shine and wind doesn't blow all the time and cannot be controlled), which must be served all the time and backed up by conventional sources.

## Slide 18: EPS operation, before

## Slide 19: EPS operation, after

## Slide 20: EPS operation, before

## Slide 21: EPS operation, after

## Slide 22: Control, before
In the centralized planning model, with smaller independent subsystems and slow changing load patterns, the need for monitoring and control was limited to keeping the system at optimal security and operation parameters in normal operation conditions and dealing with unexpected events due to malfunctions.

## Slide 23: Control, after
In the electricity market + renewable resources framework, the control and monitoring of the system must be:
    preventive, by planning the transactions on the market taking also into account the restrictions imposed by the need of having a secure operation of the system and available transport capacity
    corrective, when contingency conditions can lead do congestions on heavy loaded branches in the system, or even stability loss.

## Slide 24: RTMC of EPS
In any power system, there are many variables of interest for assessing its state, such as: bus voltages, transmission line loadings, transformer taps, power flows between areas, alarm locations.
The new operation conditions generated by interconnection on the electricity market substantially increase the amount of needed data.

## Slide 25: RTMC of EPS
A severe data overwhelm problem, even in normal operating state
Extensive changes are needed in terms of development of effective analytical and software tools.

## Slide 26: RTMC of EPS
The real time monitoring and control system (RTMCS) can be seen, from the perspective of the deregulated market system, as consisting of three interconnected layers
    the generation and physical delivery layer (generation, loads, transmission and distribution facilities and their associated embedded control and protective equipment, the system operator)
    the market layer (trading markets, physical participants, energy exchanges)
    the communication, monitoring and control layer (the sensor and measurement equipment installed in the system, the data communication network and the RTMCS commands and signals)

## Slide 27: The need of security
Power systems are continuously subject to a wide range of disturbance types, such as sudden changes in load demand, outages generator
System reliability or security is an instantaneous condition. It is a function of time and of the robustness of the system with respect to imminent disturbances.
The notion of security is the basis of all real-time monitoring and control in today’s power systems.

## Slide 28: The need of security
The working definition of security is in terms of the system state, a compact description used to summarize key information about the system; once the system state is known, it can be used to express any variables of interest.

## Slide 29: The need of security
A state is classified as being one of three possible types:
    normal, when all constraints and loads are satisfied thorough the system
    emergency, when one or more of the physical operating limits are violated (a collapse is imminent)
    restorative, where one or more of the loads are not met, partial or total blackout, but the partial system is operating in a normal state

## Slide 30: The need of security
The notion of security is defined with respect to a set of credible contingencies or unwanted events that may happen in the system. A normal state is secure if all postulated contingencies result in secure normal operation.
The main role of power system control is to maintain its secure system state, to prevent the system state from transitioning from secure to emergency over the widest range of operating conditions.

## Slide 31: RTMC systems – what they are
The RTMCS system is a collection of processes, computing equipment, measurement devices and communications used for maintaining the system secure.
Currently, EMS/SCADA systems are used

## Slide 32: RTMC systems – what they do
The RTMC system uses real-time measurements to identify whether or not the power system state is normal (monitoring).
If the state is normal, it then determines whether or not it is secure (security assessment).

## Slide 33: Electricity market and RTMCS
The unbundling of activities based on market principles increases the role and responsibility of the system operator(s) who manage(s) the grid and the RTMCS system.
There is a general agreement that the power system requires coordination to maintain its integrity and security, however there is considerable controversy on the best ways to implement such coordination under competitive conditions.

## Slide 34: Electricity market and RTMCS
With the separation of generation and transmission, their integrated control is a challenge and information availability is a major issue.
Maintaining security requires widespread availability of real-time information about physical variables; however this is not compatible with the competitive market rules.
A compromise must be made between the required level of security of the system and of the financially sensitive data

## Slide 35: Analysis tools for EPS
Physical models

## Slide 36: Analysis tools for EPS
Load flow calculations
  Computer programs
  If bus powers are known, bus voltages can be computed

## Slide 37: Analysis tools for EPS
System equivalents
    Reduction of a significant portion of the system
equivalent

## Slide 38: Analysis tools for EPS
State estimation
  Algorithms similar to load flow, use other input data (measurements)

## Slide 39: Analysis tools for EPS
P,Q
U,θ
P,Q
P,Q
P,Q
P,Q
U,θ
Pij, Qij
Pij, Qij
State estimation
    Algorithms similar to load flow, use other input data (measurements)
load flow state estimation

## Slide 40: Analysis tools for EPS
Physical models
Load flow calculations
System equivalents
State estimation
Smart Grids

## Slide 41: Next time:
SCADA systems
Thank you !