## Slide 1: Monitoring and Management of Electrical Systems - EPS element parameters for LF studies-
07.11.2014
05

## Slide 2: Electric Power Systems

## Slide 3: Load flow
Compute bus voltages using
  The EPS physical data
  The actual load conditions

## Slide 4: Load flow steps
build an one-line diagram
attach electrical parameters to the diagram
compute the bus admittance matrix
run the analysis algorithm and compute the main state variables (bus voltages, U, θ)
compute the desired auxiliary variables

## Slide 5: Load flow assumptions
simplifying assumptions that ease the computation effort, with negligible errors
    the electric and magnetic circuits are symmetrical on all three phases, for all EPS components
    the mutual influences between neighbouring EPS elements are ignored.
in steady state, EPS can be studied on a single phase only, and one-line diagrams are used.

## Slide 6: EPS conventional representation

## Slide 7: EPS conventional representation

## Slide 8: EPS – conventional representation
geographical view | Hand-drawn one-line diagram

## Slide 9: Load flow steps
build an one-line diagram
attach electrical parameters to diagram elements
compute the bus admittance matrix
run the analysis algorithm and compute the main state variables (bus voltages, U, θ)
compute the desired auxiliary variables

## Slide 10: EPS elements
EPS elements found in one-line diagrams can be grouped in two main categories:
    active elements (which require or generate power: loads, generators)
    passive elements (through which electricity just flows: lines, transformers)

## Slide 11: Buses (busbars, nodes) – input parameters
Nodes are EPS points where
    loads and generators are connected and draw or inject power in the grid
    two or more branches meet
    interconnection points between subsystems exist, where separations are made
The relevant electrical parameter is the nominal voltage
A name is recommended, but not mandatory

## Slide 12: Mathematical models for buses
NONE

## Slide 13: Buses

## Slide 14: Buses

## Slide 15
Buses in LF
Active power P
Reactive power Q
Voltage magnitude U
Voltage angle θ
    PQ buses
      know P, Q
      compute U, θ
    have load attached
    PV buses
      know P, U
      compute Q, θ
    have gen. attached
    A slack bus
      know U, θ
      compute P, Q
    have gen. or ext. grid attached

## Slide 16: Synchronous generators
electrical machines used to convert the circular mechanical motion of their rotor into alternative voltage and current flow.
Except for wind turbines, which are asynchronous machines, electrical generators are synchronous machines (operate at the same frequency thorought the system).

## Slide 17: Input parameters and mathematical models
Required LF input parameters
    the rated active power: Pn [MW]
    the nominal power factor: cos φn, cos(phi),
    the nominal phase-to-phase voltage: Un [kV]
    the synchronous direct (d) and quadrature axis (q) reactances xd, xq [p.u.] or [%]
There are two main mathematical representations for generators:
    as real voltage source
    as ideal current source

## Slide 18: The real voltage source
the three-phase rated power
the rated impedance
the generator's reactance

## Slide 19: The real voltage source

## Slide 20: PV buses
Real generators produce reactive power by varying their active/reactive output ratio (power factor).
PV buses use a variation of the generated reactive power between set minimum and maximum limits in order to keep the bus voltage at the desired setpoint.
The LF algorithm needs as input data the generated active power, the imposed voltage magnitude and the reactive generation limits, and it will compute the voltage angle and the reactive power.

## Slide 21: Synchronous Generators as PV buses
Notes: <number>

## Slide 22: Synchronous Generators as PV buses
Notes: <number>

## Slide 23: Loads
usually complex consumptions measured at station or substation transformers, aggregated from all consumers connected below the transformer.

## Slide 24: Mathematical models for load (1)
In steady state operation conditions, when there is no active or reactive power deficit, and the frequency and voltage levels are closed to nominal, loads are modeled with constant active and reactive power values, for a given time interval (usually an hour)

## Slide 25: Mathematical models for load (2, 3)
as current source
as impedance

## Slide 26: Loads in DIgSILENT Power Factory

## Slide 27: Loads in BCP Neplan

## Slide 28: Electrical lines
pathways on which electricity flows from the generation sites to the consumer sites.

## Slide 29: Input parameters for lines
The electrical parameters for the 1 km length
longitudinal
    resistance r0 [Ω/km]
    reactance x0 [Ω/km]
line-to ground
    conductance, g0 [S/km]
    capacitive susceptance b0 [Ω/km]
number of parallel circuits nc
line length l [km]

## Slide 30: Input parameters for lines
the line total parameters are computed, the impedance z and admittance y:
values differ according to the wire material used (copper, aluminium, steel of different cross-sections) and types of poles.
electrical parameters values for 1 km of wire are given by wire producers in catalogues.

## Slide 31: Mathematical models for lines
for OHL short lines (length up to 80 km), the conductance and capacitive susceptance can be neglected, and only the impedance z is used.
for medium and long lines, two models can be used:
    PI with lumped parameters
    The distributed parameters model

## Slide 32: The PI model
OHL <100 km, cables <50 km, kz=ky=1;
OHL < 250 km

## Slide 33: The PI model with admittances

## Slide 34: Lines in DIgSILENT Power Factory

## Slide 35: Lines in BCP Neplan

## Slide 36: Transformers
Transformers used in EPS can be
    power transformers
    measurement transformers
Three-phase power transformers
    2-winding transformers
    3-winding transformers
    auto-transformers

## Slide 37: Input parameters for LF
the nominal voltage on the HV winding [kV]
the nominal voltage on the LV winding [kV]
the short-circuit voltage [%]
the no-load current [%]
load or copper losses [kW]
no-load or iron losses [kW]
tap changer ratios and steps
the vector groups of windings (Y,d or Z)

## Slide 38: Input parameters for LF
Electrical parameters are computed:

## Slide 39: Transformer types
Taking as reference the power flow direction in which power flows through the transformer, the windings are named "primary" and "secondary".
When the HV winding is the primary, the transformer is of step down type.
When the primary winding is the LV winding, the transformer is of step up type.

## Slide 40: Mathematical model – Γ (gamma)
The step up transformer

## Slide 41: 2W transformers in DIgSILENT Power Factory

## Slide 42: 2W transformers in DIgSILENT Power Factory

## Slide 43: 2W transformers in BCP Neplan

## Slide 44: Next…
The bus admittance matrix and general mathematical models for load flow algorithms
Thank you !